| WCDMA 하향링크 시스템에서의 적응 하이브리드 채널 추정 기법 Hybrid Adaptive Channel Estimation in WCDMA Downlink Systems 최인호, 이용환 Inho Choi and Yong-Hwan Lee School of Electrical Engineering and INMC, Seoul National University Kwanak P. O. Box 34, Seoul, 151-744, Korea e-mail: ylee@snu.ac.kr | 제15회 신호처리합동학술대회 저자1 * and 저자2** * **강원대학교 제어계측공학과, 춘천시 효자2동 192-1 *author1@server.ac.kr and **author2@server.ac.kr |
| --- | --- |

Abstract: The receiver performance of DS-CDMA system is significantly affected by the accuracy of channel estimate. In WCDMA downlink systems, the channel information is estimated using a pilot channel called common pilot channel (CPICH). Since both the data signal and pilot signal experience the same fading, the accuracy of channel estimate can be improved by using the dedicated physical channel (DPCH) together. However, erroneous data decision in the DPCH decoding process can deteriorate the estimation performance. In this paper, we analytically designed the coefficients that combine the two channel estimates from the CPICH and DPCH by considering the DPCH data decision error. For more accurate channel estimation, the adaptive channel estimation filters are designed for the DPCH part as well as the CPICH part. Numerical results show that the proposed channel estimator outperforms the conventional pilot channel aided estimator, particularly when the channel condition becomes worse.

Keywords: WCDMA, hybrid adaptive channel estimation

# INTRODUCTION

In the third generation WCDMA systems, coherent detection is used in both the uplink and downlink. Coherent receiver inherently requires the information on the channel impulse response (CIR). There have been proposed a number of methods to estimate the CIR. One method is to use a pilot channel which is available to all the receivers [1]. The pilot channel called common pilot channel (CPICH) in the WCDMA downlink sends out continuous pilot symbols, making it possible to estimate the CIR more accurately. The other method is to use a pilot signal which is time-multiplexed with the data signal. This method is quite applicable to the uplink that has no common pilot channel. It is also possible to combine these two methods to improve the channel estimation performance in the downlink [2].

While the above two methods use known signals, it is also possible to use unknown data signal for channel estimation. Removing the modulated data part from the received signal, it is possible to get the channel information from the dedicated physical channel (DPCH). Since this method uses the decoded data signal, it is called decision-directed (DD) method. The estimation performance can be deteriorated when erroneous decision occurs in the decoding process. To alleviate this problem, the DD method can be combined with the pilot-aided scheme, resulting in a so-called hybrid channel estimation method [3,4]. A DD scheme combined with the pilot-channel-aided method is considered in [3], where the optimal combining of these two channel estimates is analyzed based on the minimum mean squared error (MMSE) criterion. Since the optimum MMSE solution requires the knowledge on the channel statistics, it may not be applicable to real situation. The use of a multistage DD scheme is considered in [4], but it may not be feasible for real applications due to the implementation complexity.

In this paper, we consider a hybrid method that combines the DD scheme with the pilot-channel-aided scheme. The adaptive channel estimator (ACE) proposed in [1] improves channel estimation performance over the fixed channel estimator, but it uses only the CPICH for channel estimation. To further improve the performance we consider the use of a hybrid ACE scheme that combines the DD and pilot-channel-aided method. We combine the two channel estimates so as to maximize the SNR of the channel estimate. It is shown that the combining parameters can be determined in some practical manner at the receiver without a priori knowledge on the channel statistics.

# WCDMA DOWNLINK SYSTEM

The received discrete-time signal at the l-th branch of the rake receiver can be represented as

(1)

where  is the spreading factor of the DPCH,  is the CPICH pilot symbol which is equal to ,  is the k-th DPCH data symbol, and  and  are the channelization codes for the CPICH and DPCH, respectively. Note that the notation  in the bracket means the chip time index and  denotes the data symbol index.  represents the cell-specific scrambling code,  is the interference term including the multipath interference, inter-cell interference and background thermal noise, and  and  are the complex-valued channel gains multiplied by transmit gain of the CPICH and DPCH, respectively, i.e.,  and . Here,  is the complex-valued channel gain of the l-th path in the k-th symbol duration and  and  denote the transmit power of the CPICH and DPCH, respectively. Thus,  where .

# CONVENTIONAL CHANNEL ESTIMATION

## Pilot-channel-aided channel estimation

To perform the channel estimation using the CPICH, the received signal needs to be despread using the CPICH channelization code. The despread signal  can be written as

(2)

where  is the spreading factor of the CPICH equal to 256 and  represents the interference term.

Since the pilot symbol  is known,  can be extracted from  by multiplying both sides of (2) by . Then the resulting signal is low-pass filtered to reduce the interference effect using a channel estimation filter (CEF). In this paper, we consider the use of a moving average (MA) finite impulse response (FIR) filter as the CEF for ease of analysis. The estimated channel gain can be obtained as

(3)

where  is the tap size of the MA CEF for the CPICH.

## Decision-directed channel estimation

The DPCH data signal can also be used for channel estimation. The procedure is similar to that using the CPICH. The only difference is that the decoded data symbol is used instead of the known pilot symbol. The DPCH-despread signal  can be written as

(4)

where  represents the interference term. Denoting the decision data by , the estimated channel gain  can be obtained as,

(5)

where  is the tap size of the MA CEF for the DPCH.

# PROPOSED HYBRID CHANNEL ESTIMATOR

Fig. 1 depicts the structure of the proposed hybrid channel estimator. In the proposed hybrid method, the channel is first estimated using a pilot-channel-aided method as (3), which is used for combining the received data signal. Then the data signal is tentatively obtained by making hard decision on the symbol combiner output. With this hard-decided data signal, the channel is estimated again using the DPCH signal as (5). Finally, we obtain the final channel estimate by combining the two channel estimates with appropriate combining coefficients  and .

It is shown that the optimum tap size  of the MA CEF for the CPICH based ACE is determined by various channel condition factors such as the SNR, Ricean factor of the propagation path and maximum Doppler frequency [1]. Since the maximum Doppler frequency is the most influencing factor affecting the optimum tap size and the DPCH and CPICH experience the same fading, we simplify the decision of  using  such that the two CEFs have the same averaging time duration, i.e.,

(6)

Since decision errors are unavoidable in real situation, these should be taken into account for combining  with . Let  be the probability of bit errors occurred by the tentative decision. Assuming that these errors occur uniformly and that the signal  is QPSK modulated, it can be shown that

(7)

where  denotes the expectation of . Thus,  in (5) can be represented as

(8)

Fig. 1.  Structure of the hybrid channel estimator.

(9)

where  is an additional interference term due to tentative decision errors with variance .

Since  from (5) can be rewritten as

(10)

the SNR  of  is

(11)

where  is the variance of . If  is much larger than , there will be few decision errors so that  is very close to zero. On the other hand, if  is much less than  due to deep fading, the second term of the denominator of (11) can be neglected. Then,  can be approximated as

.	(12)

Similarly, the SNR  of  can be calculated from (3) and (6),

(13)

where  is the variance of  and .

In the proposed hybrid channel estimation scheme, the channel estimate  is obtained by

(14)

where  and  are the combining weights. It can easily be shown that the SNR  of  is

(15)

by using Cauchy-Schwartz inequality. Thus, the optimum combining weight that maximizes  is given by

(16)

and the corresponding SNR is

(17)

The SNR gain due to the use of the hybrid method increases as  decreases. In particular, when  is fixed, the achievable SNR increases as the power ratio of the DPCH and CPICH increases. It can be shown from (3) and (10) that

.	(18)

This implies that the optimum weight  and  can approximately be determined using  and  which are available at the receiver.

# PERFORMANCE EVALUATION

To verify the proposed hybrid ACE scheme, the receiver performance is examined under two extreme channel environments: one is when =-13dB and =-3dB, and the other is when =-10dB and =9dB, where  is the total transmit power from the desired base station and  is the transmit power from other cells. The former environment corresponds to the case when the user resides near the cell boundary and the CPICH is transmitted with relatively low power. On the other hand, the latter environment corresponds to the case when the user is near the base station and the CPICH is transmitted with relatively high power. Table 1 summarizes the simulation condition.

Fig. 2 depicts the BER performance of the proposed adaptive hybrid scheme compared to other channel estimation methods; a pilot-channel-aided scheme with fixed CEF, a hybrid scheme with fixed CEF and a pilot-channel-aided scheme with adaptive CEF. Here, the term “fixed” means the use of a MA CEF with a fixed tap size corresponding to one slot time interval. The ideal case (i.e., known CIR) is also presented for comparison. It can be seen from Fig. 2 (a) that the proposed adaptive hybrid scheme outperforms the fixed hybrid scheme and the adaptive pilot-channel-aided scheme [1]. However, those four schemes have little difference in their performance for the latter channel condition as shown in Fig. 2 (b). This is mainly due to that the CPICH power is high enough to produce an accurate channel estimate without additional use of the DPCH.

Fig. 3 depicts the required DPCH power to obtain a BER of  in terms of the Doppler frequency. It can be seen that the adaptive hybrid scheme works well for a wide range of Doppler frequency. Note that similar results are obtained even when the channel has more paths, e.g., the four-path Case-3 channel.

As shown in Fig. 1, the hybrid scheme requires an additional symbol delay  due to the CEF for the DD channel estimation, requiring an additional memory corresponding to the amount of delay. However, by using an asymmetric filter with zero group delay as the DPCH CEF, this problem can be alleviated with little performance degradation. The additional computation of the hybrid scheme is mainly due to the use of the DD scheme: hard-decision, multiplication and MA filtering. Among these, the most affecting process to increase the computational complexity is the multiplication. Since the hard-decoded data bits in the DD scheme takes a value of 1 or –1, the multiplication process can be replaced with the addition process. Thus, the proposed hybrid scheme can be realized without significantly increasing the computational complexity.

# CONCLUSION

We have proposed an adaptive hybrid channel estimation scheme that uses both the CPICH and DPCH for channel estimation. The bandwidth of the CPICH CEF and DPCH CEF is adaptively controlled according to the channel condition. The optimum combining coefficients are analytically designed considering the tentative decision errors. Simulation results show that the proposed adaptive hybrid scheme outperforms the adaptive pilot-channel-aided scheme in [1] as well as the conventional fixed schemes. The performance improvement of the proposed hybrid scheme increases as the channel condition becomes worse. The proposed scheme can easily be implemented in real situation without significantly increasing the receiver complexity.

# REFERENCES

- J.- W. Choi and Y.- H. Lee, “Adaptive channel estimation in pilot channel based DS-CDMA systems- Part I: Design of the channel estimation filter, Part II: Design of the channel estimator,” IEEE J. Select. Areas Commun., submitted.

- H. Kim, K. Kim and Y. Han, “An efficient channel estimation scheme for downlink in WCDMA/FDD systems,” Proc. VTC’2001 Fall, pp. 897-900, Oct. 2001.

- S. Min and K. B. Lee, "Pilot and traffic based channel estimation for DS/CDMA systems," Electron. Lett., vol. 34, pp. 1073-1074, May 1998.

- B. H. Park, K. J. Kim, S.- Y. Kwon and K. C. Whang, “Multistage decision-directed channel estimation scheme for DS-CDMA system with M-ary orthogonal signaling,” IEEE Trans. Veh. Tech.,vol. 49, pp. 43-49, Jan. 2000.

Table 1.  Simulation condition.

|  | Value |
| --- | --- |
| DPCH | 144 Kbps (SF=16) |
| CPICH | -13dB, -10dB |
|  | -3dB, 9dB |
| Channel | Rayleigh (classic), 3GPP model (Case-1) |
| CEF | MA FIR |
| Power control | Step size: 1dB, Control period: 1 slot (0.667ms) |

(a) Ior/Ioc=-3dB,	     	(b) Ior/Ioc=9dB,

CPICH Ec/Ior=-13dB         CPICH Ec/Ior=-10dB

Fig. 2. BER performance when =20Hz.

(a) Ior/Ioc=-3dB,	     	(b) Ior/Ioc=9dB,

CPICH Ec/Ior=-13dB       CPICH Ec/Ior=-10dB

Fig. 3. Required Ec/Ior at a BER of  in the Case-1 channel.