| 전력선 통신을 위한 CPFSK 적응 변조 기법 김수관 * , 이용환** 서울대학교 전기, 컴퓨터 공학부 Adaptive CPFSK Modulation for Power Line Communications Soo-Kwan Kim *, Yong-Hwan Lee ** School of Electrical Engineering and INMC, Seoul National University *kwanksk@trans.snu.ac.kr, ** ylee@snu.ac.kr | 제15회 신호처리합동학술대회 저자1 * and 저자2** * **강원대학교 제어계측공학과, 춘천시 효자2동 192-1 *author1@server.ac.kr and **author2@server.ac.kr |
| --- | --- |

Abstract: Power-line communication (PLC) has an advantage of no additional wiring for communications, but it may not be suitable for high speed signal transmission due to the nature of power-line. In this paper we consider the use of adaptive CPFSK modulation scheme robust to harsh power-line channel condition. The modulation parameters are initialized and adjusted during the data transmission without interrupt. The performance of the proposed scheme is analyzed and verified by computer simulation.

Keywords: PLC, CPFSK, adaptive modulation

Ⅰ. Introduction

In recent, power-line communication (PLC) has been considered as one of promissiong solutions for rapidly increasing demand for multimedia services, because it can use existing power-line network without additional wiring. However, since the power-line is designed for transmission of the electricity, it does not provide channel characteristics of good quality suitable for high-speed communications. In particular, the characteristics of the power-line significantly vary depending upon the switch status (i.e., on/off) of the electrical loads [1]. As a result, it may be desirable to employ a modulation scheme robust to time-varying channel characteristics.

Recent studies have considered the use of continuous phase modulation (CPM), spread spectrum (SS) and multi-carrier modulation (MCM) as an efficient modulation scheme for the PLC.  Since the SS scheme requires large bandwidth to obtain a large processing gain, it may not appropriate for high-speed communications and it has inferior performance compared to the MCM [2]. The MCM modulates each sub-channel independently, it may be suitable for frequency selective PLC channel, appropriate for high-speed communication. However, the implementation complexity is high compared to single carrier schemes and it may require expensive analog-front-end due to high peak-to-average power ratio (PAR). In addition, the MCM is susceptible to impulsive noise in PLC environment [3]. Although the CPM has low spectral efficiency, it features low system complexity and favorable performance due to low PAR and robustness to amplitude variation and impulsive noise [3]. The CPM decreases the sidelobe of the power spectrum by means of continuously connecting the phase that contains the information. In this paper, we consider the use of CPFSK modulation as a robust modulation scheme to the variation of signal amplitude.

The research on an adaptive modulation scheme has been adopted to utilize the transceiver bandwidth efficiency in voice-band modems from late 1980’s. In wireless systems, the use of adaptive QAM modulation has been studied by changing the modulation level, channel coding rate and transmit power [4][5]. In the MCM, an adaptive modulation is employed by allocating the subcarrier bits and power depending upon the channel condition [6][7]. However, the use of CPFSK with fixed modulation parameters has been studied as a robust modulation scheme under harsh channel condition. In this paper, an adaptive CPFSK modulation scheme is designed so as to maximize the transmission rate, while providing the desired bit error rate (BER) without any interruption of the transmission when the channel condition is changed.

Ⅱ. Channel probing

It is well understood that the characteristics of the power-line channel is abruptly changed due to the switch operation of electric loads. To obtain the optimum performance, it is required to adjust the transceiver parameters according to the channel condition. As a practical channel estimation method, the use of line probing (LP) has already been applied to QAM-based voice band modems [5]. Since the CPFSK modulation scheme is much simpler than QAM, the line probing technique can effectively be applied to the PLC environment.

It is desirable for the LP signal to be generated in a simple way, while having a minimum PAR. Since we consider the use of bandwidth between 4 and 12 MHz and symbol rates of up to 1 Mbaud, it may suffice to use tone signals spaced by 0.5 MHz. The PAR of the LP tone signal can be minimized by controlling the phase of each tone. For ease of implementation, we consider the use of tone signals having or  phase. Fig. 1 depicts the frequency response of the designed LP signal, yielding a PAR of 2.56dB.

For line probing, a periodic LP signal with a period of  is repeatedly transmitted. Let  be the received signal corresponding to the -th period of the LP signal ,

(1)

where  denotes the additive noise term. Taking the discrete Fourier transform (DFT) of , we have

(2)

where  and  denote the discrete Fourier transform(DFT) of and , respectively. Letting  be the time average of , we have

(3)

where  is total averaging number. The power spectrum of the signal component can be estimated as

(4)

Assuming that the additive noise is a zero-mean random process and uncorrelated with the signal,  is an unbiased estimate with variance inversely proportional to .

The power spectrum of the noise can be estimated by eliminating the power spectrum of the signal from the power of the received signal. The power spectrum of the received signal can be estimated as

(5)

The power spectrum of the noise signal can be estimated as

(6)

Fig. 1 Frequency response of the LP signal

Fig. 2 Block diagram of the channel estimation module

Fig. 2 depicts a block diagram of the channel estimation module. Since we consider the use of 4- or 2- level CPFSK with a symbol rate of up to 1 Mbaud, the information required for determining the modulation parameters can be obtained by the LP method.

Ⅲ. Adaptive CPFSK modulation

A CPM signal  can be expressed as [9]

(7)

where  represents the symbol energy,  is the symbol duration time,  is the carrier frequency and  is the information phase  represented as

(8)

Here  is the peak frequency deviation,  is the modulation index equal to ,  denotes the phase accumulation of the symbols up to time , i.e.,

(9)

and  is the impulse response of the phase shaping pulse defined as

(10)

The use of  keeps the FSK tone signals orthogonal, appearing to be optimum in additive white gaussian channel. However, this may not be optimum in the frequency selective power-line channel. The use of  less than 1.0 may result in a BER performance better than the use of . If the received FSK tone signals have equal power with the use of power control, the use of  provides nearly optimum performance.

Although little SNR gain is obtained by controlling the FSK modulation level, the modulation level control can be used to avoid performance degradation due to frequency selective nulls. The SNR gain can be obtained by controlling the symbol rate , since the detection bandwidth  is proportional to . That is, the received SNR  can be approximated as [10]

(11)

(12)

It can be seen that we can obtain 3dB SNR gain by reducing the symbol rate by half.

To provide optimum performance, the received SNR  of each tone is estimated using the LP method at the beginning of the operation. The LP finds out the signal bandwidth that provides the maximum average SNR. Since the channel is not ideal, we apply the power control to each tone. After the bin power control, the average SNR can be represented as

(13)

where  is the maximum symbol rate,  is the current symbol rate,  is the average SNR and  is the achievable average SNR with the symbol rate control in the receiver.

If the difference between ’s in the selected bandwidth is larger than the maximum amount of the gain adjustment, , it may be desirable to find out another bandwidth that has average SNR with the next largest value. This procedure goes until the difference become less than . If such a bandwidth is not found, the procedure is repeated after reducing the symbol rate by half. Here the value of  needs to be determined by considering the sidelobe effect of the tone to the adjacent tones and the dynamic range of the power amplifier.  If

(14)

the transmit signal power is controlled so that the received signal has tones with equal power. Since the transmit power should be unchanged with the power control, the gain  for each tone should satisfy

(15)

If  is less than the SNR required for specified BER, it is required to control the symbol rate.

Ⅳ. Performance evaluation

To evaluate the performance of the proposed adaptive modulation scheme, we consider a CPFSK based PLC modem with a maximum transmission of 2 Mbps, using frequency band between 4 and 12 MHz.  The PLC modem employs 4- or 2-level CPFSK modulation at a symbol rate of 0.25, 0.5 or 1Mbaud depending upon the channel condition. Fig 3 depicts the structure of the power-line network considered for performance evaluation. Fig. 3 (b) and (c) illustrate the frequency response of the channel when only PC 1 is on and others are all off, and all the loads are switched on, respectively.

Fig. 4 depicts the BER performance when the proposed scheme with  is applied to the channel shown in Fig. 3. It can be seen that the use of bin power control significantly improve the receiver performance and that the use of halved symbol rate can provide an SNR gain of 3dB.  It can also be seen that there is a performance gap of approximately 3dB compared to the AWGN case. This is mainly due to that the orthogonality of tones is corrupted by the intersymbol interference (ISI).

Fig. 5 depicts the receiver performance in terms of the transmission rate and BER when the proposed scheme is applied to the channel condition Fig. 3(b). It can be seen that the adaptive CPFSK system provides the required  BER performance by adjusting the symbol rate and modulation level according to the SNR condition.

(a) Example of the power-line network

(b) PC1 on, others off

(c) All swithes on

Fig. 3 Example of the power-line network

Fig. 4 BER performance

Fig. 5 Performance of adaptive modulation scheme

Ⅴ. Conclusion

In this paper, we have proposed an adaptive CPFSK modulation scheme that can transmit the data at a maximum rate of 2 Mbps without interrupt under time-varying power-line channel condition. The modulation parameters are initialized by estimating channel information using the line probing technique. The modulation parameters are adjusted to provide a desired BER performance without interrupting the data transmission when the channel condition is suddenly changed.  Simulation results show that the adjustment of each tone power, symbol rate and modulation level can provide performance quite robust to time-varying power-line channel condition.

References

[1] M. Zimmermann and K. Dostert, “An analysis of the broadband noise scenario in powerline networks,” Proc. ISPLC2000, pp.131-138, Limerick, April 2000.

[2] E. D. Re and R. Servalle, “Comparison of CDMA and OFDM systems for broadband downstream communications on low voltage power grid,” Proc. ISPLC2000, pp.47-52, April 2000.

[3] K. Dostert, Powerline communications, Prentice-Hall, 2001.

[4] T. Ue and K. Hamaguchi, “Symbol rate and modulation level-controlled adaptive modulation/TDMA/TDD system for high-bit-rate wireless data transmission,” IEEE Trans on. Vehi. Tech., vol. 47, pp.1134-1137, Nov.1998.

[5] A. J. Goldsmith and S. G. Chua, “Variable rate variable-power M-QAM for fading channels,” IEEE Trans. Commun., vol.45, pp.1218-1230, Oct. 1997.

[6] C. H. Yih and E. Geraniotis, “Adaptive modulation, power allocation and control for OFDM wireless networks,” PIMRC 2000, vol.2 , pp. 43-47,  2000.

[7] M. R. Souryal and R. L. Pickholtz, “Adaptive modulation with imperfect channel information in OFDM,” ICC 2001, vol.6, pp.1861-1865, 2001.

[8] V. Eyuboglu and P. Dong, “Line Probing Modem,” U.S. Patent  No.5048054, Sept. 1991.

[9] J. G. Proakis, Digital Communications, McGraw-Hill, New-York, 1995.

[10] B. Sklar, Digital Communications, Prentice Hall, NJ, 1988.